N	USB	L0
L31		N
N	32 channel dimmer / Send commands over USB virtual serial port, baud of 115200. / Commands end with newline „\n“. / „I23\n“ turns 23. channel on, / „O14\n“ turns 14. channel off, / etc. / Commands „I\n“ and „O\n“ without numbers switches all outputs. / < 0,9 A / 200 W per output / < 16 A / 3 680 W per device / Mains electric work must be done by qualified electrician. Do not touch after connecting. / Tech-thing OÜ 2014	L1
L30		N
N		L2
L29		N
N		L3
L28		N
N		L4
L27		N
N		L5
L26		N
N		L6
L25		N
N		L7
L24		N
N		L8
L23		N
N		L9
L22		N
N		L10
L21		N
N		L11
L20		N
N		L12
L19		N
N		L13
L18		N
N		L14
L17		N
N	230 VAC	L15
L16		N