L0	N	L1	N	L2	N	L3	N	L	N
Dimmer outputs								230VAC
4 channel USB dimmer / Send commands over USB virtual serial port, baud of 115200. Commands end with newline „\n“. „I23\n“ turns 23. channel on, „O14\n“ turns 14. channel off, etc. Commands „I\n“ and „O\n“ without numbers switches all outputs. / < 0,9 A / 200 W per output. < 16 A / 3 680 W per device / Mains electric work must be done by qualified electrician. Do not touch after connecting. Tech-thing OÜ 2014
USB